## Slide 1
高性能计算程序设计
任课教师：
黄聃（Huang，Dan）

## Slide 2
CUDA OPTIMIZATION, PART 1
NVIDIA Corporation

## Slide 3: OUTLINE
Architecture:
  Kepler/Maxwell/Pascal/Volta
Kernel optimizations
  Launch configuration (use lots of threads)
Part 2 (next session):
  Global memory throughput (use memory efficiently)
  Shared memory access
Most concepts in this presentation apply to any language or API on NVIDIA GPUs

## Slide 4: EXECUTION MODEL
    CUDA threads are executed by scalar processors (Lane of SIMD processor)
    Thread blocks are split to warps and executed on multiprocessors (SIMD processor) in SIMT.
    Several concurrent thread blocks can reside on one SIMD processor (when the number of thread blocks greater than multiprocessors) - limited by SIMD processor resources (shared memory and register file)
    A kernel is launched as a grid of thread blocks
Software
Hardware
CUDA Thread
Scalar Processor
Thread Block
Streaming Multiprocessor
...
Grid
Device
Lane of SIMD processor
SIMD processor
Warp
SIMD thread

## Slide 5: WARPS 线程束
A thread block consists of thread warps
A warp is executed physically in parallel (SIMD) on a multiprocessor
Thread Block
Streaming Multiprocessor
SIMD Processor
32 CUDA Threads
32 CUDA Threads
32 CUDA Threads
...
Warps
=

## Slide 6: LAUNCH CONFIGURATION: SUMMARY
Need enough total threads to keep GPU busy
  Typically, you’d like 512+ CUDA threads per SIMD Processor
    More if processing one fp32 element per thread
  Of course, exceptions exist
Threadblock configuration
  Threads per block should be a multiple of warp size (32)
  SIMD Processor can concurrently execute at least 16 thread blocks (Maxwell/Pascal/Volta/Ampere: 32)
    Really small thread blocks prevent achieving good occupancy
    Really large thread blocks are less flexible
    Could generally use 320-512 threads/block, but use whatever is best for the application